## Slide 1
UNDERWATER VEHICLE DESIGN CHALLENGE
TEAM SUBNAUTICA

## Slide 2
  3D Mapping: Advanced Sonar for terrain modeling in GPS-denied areas.
  Anomaly Detection: Identifies hazardous conditions like volcanic vents.
  Data Logging: Continuously records pH, temperature, pressure, and salinity.
  In-situ Analysis: Analyzes soil and water samples for minerals and pollutants.
  Mobility: Navigates turbulent underwater environments.
  Ecological Safety: Ensures no disturbance to ecosystems.
  Reliability: Designed for missions up to two days.
Develop a Remotely Operated Vehicle (ROV) for exploring underwater caves and sinkholes
Create a multifunctional ROV for advanced underwater exploration while prioritizing ecological safety and non-invasive studies.
OVERVIEW
CHALLENGE OVERVIEW
KEY FEATURES
MISSION STATEMENT

## Slide 3
MECHANICS
FRAME STRUCTURE (DIAMOND-TYPE GEOMETRY)
  Rectangular space-frame using anodized Al-6061-T6, with four corner uprights and top/bottom decks connected via cross-members and X-/K-bracing.
  Indexed hard-points on the front ring and slotted rails on the lower deck for payload flexibility and CG tuning.
ELECTRONICS HOUSING (DUAL-CYLINDER DESIGN)
  Central “main cylinder” comprises a 4-inch acrylic watertight tube with aluminum end caps, housing electronics and sensors.
  Balanced pressure design: inner electronics cylinder suspended via an electronics tray (ABS + aluminum spacers) inside the outer tube, ensuring uniform pressure distribution and easy service access

## Slide 4
  6-DOF vectored thrusters mounted on gusseted bosses:
    Surge (forward/back): mid-height, 20–30° toe-in for
smooth navigation in narrow passages.
    Sway (lateral): front-side mounts for fine side movement
control, with guards to protect against impact.
    Heave (vertical): placed below the CG for stable vertical
motion and minimal pitch coupling.
DUAL MANIPULATOR ARMS
  Left: Pincher arm: Two opposing jaws (like claws) operated by servo motors to pick up rocks, shells, or biological samples
  Right: cup arm: Scooping mechanism at end with internal teeths to scratch off soil sample from hard surface
THRUSTER PLACEMENT
BALLAST & STABILITY CONTROL
  Compact ballast tanks:
    integrated at the base of the frame which serves as backup for thruster failure
  Buoyancy foams:
    Rigid, pressure resistant and retains trapped air inside water
    Neutral buoyancy point, thus thrusters alone can be used for ascending and descending

## Slide 5
  Core Intelligence: The NVIDIA Jetson AGX Orin is the central processing unit, enabling autonomous navigation and data fusion.
  Navigation & Mapping: A DVL, IMU, and Sonar Array provide precise navigation in GPS-denied environments and create 3D maps.
  Environmental Analysis: A suite of sensors including a Water Quality Sonde, pH Sensor, Raman Spectrometer, and pXRF collect critical environmental and chemical data.
  Vision & Data: An integrated low-light Camera provides visual feedback, with all data logged to onboard storage.
ELECTRONICS
SUBSYSTEM

## Slide 6
  Primary Source: A surface-supplied tether provides continuous power.
  System Stability: Intelligent distribution with failsafe converters and real-time monitoring ensures regulated power to all subsystems.
  Contingency: Upon tether failure, a backup battery initiates an automated ascent and recovery protocol.
  Primary Link: The hardwired tether provides a high-bandwidth, low-latency connection for robust real-time control and data telemetry.
  Backup Link: An Acoustic Modem activates if the tether fails, transmitting distress signals to ensure vehicle recoverability.
COMMUNICATION SYSTEM
POWER & COMMUNICATION
POWER SYSTEM

## Slide 7
CAVE MAPPING AND RECONSTRUCTION
EXPLORING THE UNSEEN DEPTHS
REAL TIME 3D MAPPING
SENSORS FUSION FOR PRECISION
Sensor data fusion, probabilistic modeling, and iterative refinement ensure AUV receives a real-time, continually improving model of the exploration area. This process converts raw sonar point cloud data into a solid mesh model, providing a clear and comprehensive reconstruction of the underwater environment.
  Sonar Array: Provides near-360-degree acoustic data for continuous 3D map construction (range up to 200m).
  IMU: Offers stable orientation and motion tracking for dead reckoning.
  DVL: Corrects IMU drift with precise seafloor velocity measurements, maintaining positional integrity.
Our ROV utilizes a real-time 3D Simultaneous Localization and Mapping (SLAM) algorithm to continuously track its position while building intricate point cloud maps of GPS-denied underwater environments. This ensures a dynamic, high-resolution understanding of its surroundings.

## Slide 8
  Thermal Sensors: Detect rapid temperature increases above 20∘C to identify volcanic vents.
  pH Sensors: Signal acidic water by detecting a pH level below 6.0, often found near hydrothermal vents.
  Chemical Sensors: Identify hazardous regions by detecting high concentrations (over 5 mM) of sulphide, a key indicator of hydrothermal vents.
  Vectoring Thruster Control: Uses six-degrees-of-freedom thrusters for immediate and precise course changes away from hazards.
  Intelligent Path Planning: Dynamically reroutes the mission using a modified A* algorithm to find the safest and shortest alternative path.
  Failsafe Protocol: Executes an emergency ascent or a pre-defined recovery program if no safe avoidance path is available.
AVOIDANCE
ANOMALY ANALYSIS
DETECTION

## Slide 9
Our methodology is built around a real-time processing loop that runs continuously on the AUV during its autonomous survey.
DATA LOGGING
ONBOARD SYSTEM WORKLFOW
SENSE
FUSE&
REFINE
ANALYSE&
MAP
LOG
While navigating, the AUV's DVL and sonde constantly acquire raw data streams from the environment.
The onboard NVIDIA Jetson processor immediately fuses these streams. The data is simultaneously filtered to remove sensor noise and anomalies.
The cleaned, fused data is instantly fed into our ROS 2 software stack. This performs environmental modeling and renders a detailed, layered map of the environment as it is being discovered.
The final, processed output—containing precise coordinates, water quality, and current vectors—is written to the onboard logger. This loop repeats at a high frequency throughout the mission.

## Slide 10
  Inlet pipe (1 cm ID, abrasion-resistant PTFE/Santoprene)
  Peristaltic pump: draws 4–6 L/min, prevents backflow
  Stone trap / pre-filter: captures >5 mm grains
  Anodized Al - 6061 -T6, pressure-balanced for ~300 bar
  Holds fixed slurry volume for in-situ study
  Integrated sensors:
    pH, Temperature
    Ion-selective electrodes (NO₃⁻, NH₄⁺, Cl⁻, heavy metals)
    Gas/chemical probes (O₂, H₂S, pollutants)
    Raman + XRF → molecular & elemental composition
  Second peristaltic pump discharges sample
  Dual check valves = no contamination, no seawater intrusion
  Cycle: Fill → Seal & Analyze → Expel
1
2
3
SOIL-WATER COLLECTION & ANALYSIS
INLET & SAMPLE HANDLING
OUTLET & FLOW CONTROL
ANALYSIS CHAMBER

## Slide 11
  Ultrasonic Transducers: Measures oil slick thickness.
  Laser Raman Spectrometer: Identifies specific oil types.
  Chemical Sensor Arrays: Confirms presence of pollutants.
ENVIRONMENTAL SENSING & ANALYSIS
HYDROCARBON CONCENTRATION
MINERAL
ANALYSIS
DATA &
NAVIGATION
  Microelectrodes: Analyzes dissolved mineral ions and gases directly from the sediment.
  pXRF: Conducts on-site elemental analysis of rock and sediment samples.
  Integrated Navigation (DVL/IMU): Tracks precise location.
  Automated Sampling: Collects data on a programmed grid.
  Data Logging: Creates a time-stamped, 3D georeferenced map.

## Slide 12
MARINE BIOLOGICAL ANALYSIS
KEY CONSTRAINTS
SOLUTION
TECHNICAL IMPLEMENTATION
  Minimal disturbance (hydrodynamic, acoustic, optical).
  Non-contact eDNA collection with accurate tracking mechanism.
  Functionality in turbid/low-light conditions.
  Remote Observation: Ultra-low-light imaging, multispectral filters, passive acoustics.
  eDNA Sampling: Peristaltic pump with sterile filters.
  Preservation: Sealed cassettes with unique IDs.
  Low-Disturbance Operations: Ducted thrusters and red-spectrum lighting.
  Architecture: Modular design with interchangeable pods.
  Sensors: 4K low-light camera.
  Fluidics: Pump for sterile water sampling with anti-contamination protocols.
  Software: Automated sampling and data logging.

## Slide 13
SUBSYTEM FAILURE & RECOVERY
COMMUNICATION FAILURE
POWER SYSTEM FAILURE
SENSOR &
DATA FAILURE
SOFTWARE &
CONTROL FAILURE
  Problem: System crash or stall.
  Solution: Watchdog timer initiates a system reset or triggers the emergency buoyancy system.
  Sensor: Watchdog Timer / Acoustic Modem Signal Strength.
  Problem: Lost link to surface.
  Solution: Automated "Return to Surface" protocol triggers after a preset time.
  Sensor: Communication Status Sensor.
  Problem: Main power loss.
  Solution: Redundant emergency battery powers essential systems (buoyancy, pinger).
  Sensor: Voltage/Current Sensor.
  Problem: Key sensor malfunction.
  Solution: Mutiple sensors and a self-correction routine. Onboard non-volatile memory for data recovery.
  Sensor: N/A (Software-based).

## Slide 14
STRUCTURAL FAILURE
TETHER SNAGS
MOBILITY SYSTEM FAILURE
  Problem: Water leak.
  Solution: Sensors detect water ingress, triggering immediate buoyancy ascent.
  Sensor: Water Leak Sensor.
  Problem: ROV stuck.
  Solution: Use tether as tow line. Emergency tether release if snagged, followed by buoyancy ascent.
  Sensor: Tether Tension Sensor.
  Problem: Tether severed or permanently snagged.
  Solution: Emergency tether release mechanism, followed by buoyancy ascent and separate recovery. Onboard battery for short-term power.
  Sensor: N/A (Part of Mobility System Failure).

## Slide 15
HYPER-AUTONOMOUS MISSIONS
LONG-TERM HABITAT MONITORING
ADAPTIVE DESIGN &
BIO-INSPIRED MOVEMENT
IMMERSIVE MIXED-REALITY CONTROL
FUTURE PROSPECTS

## Slide 16
THANK YOU
FOR YOUR ATTENTION